## Slide 1: RIPE 72 IPv6 WG Community Wi-Fi and IPv6
John Jason Brzozowski

## Slide 2: Background
IETF I-D draft-ietf-v6ops-unique-ipv6-prefix-per-host
Initially to deploy IPv6 support for community Wi-Fi
  Applies to other environments including environments where shared media is utilized
Focus on IPv6 only for UE
  And IPv6 for the underlying transport
Ensure there is no impact to network performance care of IPv6

## Slide 3: Community Wi-Fi and IPv6
Internet
Private SSID
Broadband
Access Network (CMTS)
Wi-Fi Aggregator
Public SSID
IPv6 only transport
Dual stack Wi-Fi
Dual stack Wi-Fi
Unique IPv6 /64 (not PD)
IPv6 only transport
Single broadband /64 (via PD)

## Slide 4: Overview
Leveraging unique IPv6 prefixes per device
  /64
Maximize coverage for IPv6 only
  IPv4 is out of scope but is present
Addressing
  SLAAC
  Privacy and temporary addressing
  No stateful DHCPv6 for address assignment
Configuration
  RDNSS
  Stateless DHCPv6
Initially focused on hosts, not routers

## Slide 5: IPv6 Plumbing
IPv6 Router Discovery
  Ensure widest range of compatibility for Wi-Fi capable devices
  Leverage RDNSS [RFC6106] to enable IPv6 only experiences
IPv6 Neighbor Discovery
  Minimize impact of link local communication impact to Wi-Fi (access) network
  See I-D for specific attributes and configuration options
Overarching objective is an IPv6 only experience

## Slide 6: Futures
Incorporate comments and edits based on WG feedback to date
Update based on initial trials and deployment
Post initial deployment assess support for IPv6 prefix delegation