## Slide 1: Interconnection in the Nordics
Lasse Jarlskov
RIPE72 - Copenhagen

## Slide 2: The Nordics
Scandinavia explained:
https://youtu.be/TsXMe8H6iyc
Interconnection in the Nordics, RIPE Copenhagen 2016

## Slide 3: The Countries
Denmark
Sweden
Norway
Finland
Iceland
Self-governing regions:
Greenland (Denmark)
Faroe Islands (Denmark)
Åland (Finland)
Interconnection in the Nordics, RIPE Copenhagen 2016
Agenda
The Connectivity
  How to connect.
The Markets
  Who to connect with.
The Datacentres and IXPs
  Where to connect.

## Slide 4: Country Overview
And top broadband-operators / incumbents
Interconnection in the Nordics, RIPE Copenhagen 2016
Denmark | Sweden | Norway | Finland | Iceland | Greenland | Faroe Islands | Åland
Copenhagen | Stockholm | Oslo | Helsinki | Reykjavik | Nuuk | Torshavn | Mariehamn
5,7M | 9,9M | 5,2M | 5,5M | 300K | 56K | 50K | 26K
.dk | .se | .no | .fi | .is | .gl | .fo | .ax
Lego | IKEA | Fjords | Lakes | Geysers | Polar bears | Tunnels | Kurtis!
TDC | Telia | Telenor | Sonera/ Elisa | Siminn | Tele-Greenland | Faroese Telecom | 

## Slide 5: Highlights
Or ”Where to PoP?”
Stockholm
  Interconnection hub of the Nordics
  Lots of russian carriers peering here
Copenhagen
  Gateway to the Nordics
  40% of swedes live closer to Copenhagen than to Stockholm
Helsinki
  Gateway to the east (Russia, China and the baltics)
Reykjavik
  Free power and cooling
  Expensive connectivity

## Slide 6: The Connectivity in Scandinavia+Finland
Main routes:
Copenhagen-Stockholm-Oslo-triangle
Copenhagen-Hamburg
Stockholm-Helsinki-Tallinn-Stockholm
Caveats:
Copenhagen choke-point. (5km)
Alternatives:
Stockholm-Gothenburg-Hamburg
Oslo-Kristiansand-Hamburg
Helsinki-Moscow
Helsinki-Talinn-Warsaw
New developments (sea-cables):
C-LION; Helsinki-Rostock
Denmark – United Kingdom
http://cinia.eu/en/c-lion
Interconnection in the Nordics, RIPE Copenhagen 2016
Towards Warsaw
Towards Moscow

## Slide 7: The connectivity - Atlantics
Greenland connect
Interconnection in the Nordics, RIPE Copenhagen 2016
FARICE

## Slide 8: The Markets
Residential broadband subscriptions (incl. mobile broadband)
Interconnection in the Nordics, RIPE Copenhagen 2016
Denmark | Sweden | Norway | Finland
Copenhagen | Stockholm | Oslo | Helsinki
5,7M | 9,9M | 5,2M | 5,5M
.dk | .se | .no | .fi
Lego | IKEA | Fjords | Lakes
TDC (AS3292) | Telia (AS3301) (part of AS1299) | Telenor (AS2119) | Elisa (AS6667)
Stofa (AS39642) | Telenor (AS2119) | GET (TDC) (AS41164) (part of AS3292) | Sonera (AS1758) (part of AS1299)
Telenor (AS9158) (part of AS2119) | Tele2 (AS1257) | NextGenTel (AS15659) | DNA (AS16086)
Telia (AS3308) (part of AS1299) | 3 (AS44034) | Altibox (AS29695) | Finnet (AS47605)
 | ComHem (AS39651) |  | 
Notes: DK: TDC (57%), Stofa (12%), Telenor (7%), Telia (3,8%), Rest: 20% on smaller players
SE: TeliaSonera (35%), Telenor (21%), Tele2 (18%), 3 (12%), ComHem (5%), Rest 9% on smaller players
NO: Telenor (42,3%), GET (16,9%), NextGenTel (7,5%), Altibox (?)
FI: TeliaSonera (31%), Elisa (32%), DNA (24%), Finnet (11%), AS47605

## Slide 9: The Markets
Notable aggregators - local wholesale IP transit-providers
Interconnection in the Nordics, RIPE Copenhagen 2016
Denmark | Sweden | Norway | Finland
Copenhagen | Stockholm | Oslo | Helsinki
5,7M | 9,9M | 5,2M | 5,5M
.dk | .se | .no | .fi
Lego | IKEA | Fjords | Lakes
TDC (AS3292) | Telia (AS3301) (part of AS1299) | Telenor (AS2119) | Elisa (AS6667)
Nianet (AS31027) | IP-only (AS12552) | TDC (AS3292) | Sonera (AS1758) (part of AS1299)
GlobalConnect (AS9158) | Bahnhof (AS8473) | Broadnet (AS15659) | DNA (AS16086)
Telia (AS3308) (part of AS1299) | TDC (AS3292) |  | Finnet (AS47605)
 | Bredband2 (AS29518) |  | 

## Slide 10: IXPs and datacentres
Interconnection in the Nordics, RIPE Copenhagen 2016
IXPs:
COMIX (COpenhagen/Malmö Internet eXchange)
  Operated by Netnod
  InterXion CPH, GlobalConnect, Telia Telehouse, Malmö/B, Malmö Vestergatan
  ~40 networks, ~55G, increasing
  Fun fact: 40% of swedes live closer to Copenhagen than to Stockholm
DIX (Danish Internet eXchange point)
  Operated by the Technical University
  Locations: Lyngby, InterXion CPH, Skanderborg
  44 networks, ~70G, declining/stable
Datacentres:
InterXion CPH
  Known operational level and quality
  Not on the direct fiber-path for international connectivity
GlobalConnect – Hørskætten
  Aggregation-point for (almost) all small local networks.
  On direct international fiber-paths.
  No remote-hands-service.
Telia Telehouse – Sydvestvej
  The legacy telco-site
  Where most international fiber lands.
  Almost(?) completely full
Copenhagen

## Slide 11: Local Datacentres and IXPs
Stockholm
Netnod Stockholm
  Two LANs – mandatory to connect to both
    ”Why sell one port, when you can sell two at double the price”
  About 1100 Gbps across both LANs
  Participants from Russia, Finland and the Baltics
STHIX
  Independent IXP in Stockholm
Netnod COMIX
  Copenhagen/Malmö metro-region
  Participants from Denmark and Sweden
    Fun fact: ”40% of Swedes live closer to Copenhagen, than to Stockholm”
Netnod Gothenburg, Sundsvall, Luleå
  Local participants
InterXion Stockholm, Kista
TeleCity Stockholm 1, Bromma
  Both sites are equally popular
  ~10 km apart
  Local Netnod presence (WDM) in both
TeleCity Stockholm 2, Sköndal
  Far south of Stockholm – no cross-campus cross-connects, 20+ km
Digiplex, Upplands Väsby
  Up and coming.
IXPs:
Datacentres:

## Slide 12: Local Datacentres and IXPs
Oslo
Interconnection in the Nordics, RIPE Copenhagen 2016
IXPs:
Datacentres:
The University of Oslo runs six IXPs:
  NIX1, Oslo
    60 Gbps
  NIX2, Oslo
    10 Gbps
  Also in Bergen, Trondheim, Stavanger and Tromsø – mainly relevant for local carriers trying to reduce latencies in a vast country
Bulk is threatening to start a new IXP in HMG9
Digiplex, Ulvenveien (aka. ”Ulven”, The Wolf)
  Well connected with lots of local providers.
Bulk Infrastructure, Hans Møller Gassmansvei 9 (aka. HMG9)
  Well connected with lots of local providers.
  New owner with fantastic/fanatic visions causing uncertainties about future pricing.
    Some local providers looking to vacate.
Vault, Økernveien

## Slide 13: Local Datacentres and IXPs
Helsinki
Interconnection in the Nordics, RIPE Copenhagen 2016
IXPs:
Datacentres:
FICIX2, Helsinki
  26Gbps
FICIX1, Espoo (suburbs of Helsinki)
  10Gbps
Regional exchanges:
FICIX3, Oulu
TREX, Tampere
Telecity, Helsinki,
Digita, Pasila
Nebula, Kiviaidankatu
Technopolis Innopoli (FICIX1)
  legacy