## Slide 1: Blackholing at IXPs
¹ INET, TU Berlin
² R&D, DE-CIX
On the Effectiveness of DDoS Mitigation in the Wild
Christoph Dietzel ¹ ², Anja Feldmann ¹, Thomas King ²
RIPE 72

## Slide 2: DDoS Attacks Remain a Serious Threat

## Slide 3: What is Blackholing?
Operational technique to counter DDoS attacks
Triggered directly by IP owners through BGP
Last resort to protect upstream/peering link or own network
Since a few years also at IXPs (DE-CIX, MSK-IX, NETIX, NIX-CZ, …)

## Slide 4: Recap – Blackholing at IXPs
datacenter
network
next hop:
IP D
next hop:
IP D
next hop:
IP D
next hop:
IP BH
AS D
IXP

## Slide 5: Recap – Blackholing at IXPs
datacenter
network
next hop:
IP BH
next hop:
IP BH
next hop:
IP D
next hop:
IP BH
AS D
IXP

## Slide 6
Is it frequently used and how is it used?
What is the impact on traffic?
How can we improve blackholing?

## Slide 7: Blackholing Usage Analysis – Active Announcements
About 23,000 announcements
Stable number of active /32 blackholes (~1200)
Also stable number of less specifics /31 - /18 (~50)
What about new announcements?

## Slide 8: Blackholing Usage Analysis – New Announcements
High variance in new announcements
Spikey less specifics (/31 - /18)
Blackholing is indeed widely used!
But which prefix sizes?

## Slide 9: Blackholing Usage Analysis – Prefix Length
Mainly /32 announcements (97%)
/24 - /31 account for 2.5%
9 announcements for < /24
More specific acceptance needed
Announced for how long?
Notes: 22,994 blackholing BGP announcements

## Slide 10: Blackholing Usage Analysis – Active Duration
Active duration per prefix (/32)
Majority is short-lived (~50% <= 3 hours)
Longest observed announcement 76.31 days

## Slide 11: Blackholing Usage Analysis – Active Duration
Majority is short-lived
Also very long living announcements
Could be the same prefix?!

## Slide 12: Blackholing Usage Analysis – Re-Announcements per Prefix
7,864 unique prefixes
Most prefixes announced once (10%), or between two and three times (15%)
Outliers spread from 10 to 100, max 623
Notes: 7, 864 unique prefixes
10% once, 15% between two and three times.

## Slide 13: Case Study - Impact on Traffic
Traffic for one /32
Traffic rises up to 17.6 Gbit/s
Traffic is reduced by one third

## Slide 14: Summary
23,000 announced blackholes (over a three month period)
Stable number of 1200 active blackholes
Observed least specific was a /18
Very diverse announcement patterns (frequency, duration, …)
Succeeds in mitigating large DDoS attacks
Full paper at http://www.net.t-labs.tu-berlin.de/papers/DFK-BIXPO-16.pdf

## Slide 15: Comments? Questions?